## Slide 1: Global Precipitation Measurement
Walt Petersen
GPM Deputy Project Scientist for Ground Validation
Chief, Earth Sciences Office of Field Support
NASA’s Goddard
Space Flight Center
CoCoRaHS Webinar
February 18, 2015
Notes: Title slide

## Slide 2
Notes: Rain affects everyone on Earth
-- rain, snow and ice are one of the primary sources of freshwater for people around the world

## Slide 3
Notes: Four applications of GPM data (snowstorm in Ontario, Canada; storm track of Hurricane Katrina; landslide vulnerability map from TRMM data; Cedar Rapids, Iowa, flooded in 2008)
GPM applications include
-- predicting storms and getting an accurate measurement of snowfall
-- providing new data to better understand how hurricanes move and intensify
-- providing information about what areas are vulnerable to landslides
-- predicting floods

## Slide 4
Notes: Four more Applications of GPM data (water faucet for drinking water, Famine Early Warning System, World’s Freshwater Supplies, life cycle of Schistosomiasis correlated to flood events)
-- snowpack and rainwater replenish aquifers and reservoirs used for drinking water and water for agriculture
-- rain data aids projections of freshwater availability around the world
-- in turn, this helps with agriculture projections and famine early warning systems, especially in Africa where rainfall is scarse in many regions
-- knowing where and when it rains also helps with world health in the cases of diseases that flourish when rainwater is high. In the example above, snails that are carriers of Shistosomiasis reproduce rapidly in wet conditions. Their presence, and the spread of Schistosomiasis, is correlated with high rainfall.

## Slide 5
Notes: Water cycle
-- water endlessly moves through the water cycle
-- precipitation is the part that we can see and touch the most easily
-- the water cycle is part of the wider Earth and climate system
-- understanding the processes of how storms form, and how rain and snow behave in the atmosphere improves our understanding of our planet

## Slide 6
Notes: GPM Core Observatory
-- GPM Core Observatory provided by NASA and Japan Aerospace Exploration Agency (JAXA)
-- The GPM Core Observatory was built at NASA’s Goddard Space Flight Center and is the largest satellite ever built and assembled at Goddard
-- has two advanced instruments, a Dual-frequency Precipitation Radar (DPR) and a GPM Microwave Imager (GMI)
-- the data collected onboard the GPM Core Observatory will serve as the reference standard for the data collected by the constellation satellites, so it can all be combined into a consistent precipitation product available globally every 3 hours

## Slide 7
Notes: GPM Constellation
-- Satellites can get the view from above and see the whole world
-- The GPM mission is an international satellite mission led by NASA and the Japan Aerospace Exploration Agency (JAXA)
-- It is a multi-country partnership that collects rain data from multiple satellites to get a global map of rain data every three hours
-- The GPM Core Observatory is the satellite that unifies the measurements into a global data set
--The other satellites that contribute data to the GPM mission each have their own scientific or operational goals

## Slide 8: GPM Core Satellite Key Instruments
GPM Microwave Imager (GMI)
Dual Frequency Precipitation Radar (DPR)

## Slide 9
How the Instruments Work
http://svs.gsfc.nasa.gov/goto?11253
Notes: Video: What the instruments measure inside clouds
URL: http://svs.gsfc.nasa.gov/goto?11253
-- animation begins with GMI. Purple upward pulse indicates naturally emitting energy from the ground and precipitation
-- each channel on the instrument is sensitive to different types of precipitation
-- lower frequency (10 to 37 GHz) channels are more sensitive to raindrops, middle frequency channels (37 to 166 GHz) to both liquid and ice particles, higher frequency channels (166 to 183 GHz) to snow and ice
-- the DPR sends down two pulses. The Ka-band is more sensitive to ice in the upper part of the cloud and the Ku-band is more sensitive to liquid rain lower in the cloud

## Slide 10
How the Instruments Scan
http://svs.gsfc.nasa.gov/goto?4016
Notes: Video: The GPM Core Observatory’s instruments collecting data
URL: http://svs.gsfc.nasa.gov/goto?4016
-- this video shows how the DPR and the GMI collect precipitation data
-- first it shows the Ka-band radar, whose ground swath (75 miles or 120 km) is nested inside the Ku-band radar’s swath (152 miles or 245 km). They make 3D observations of precipitation
-- next, the GMI data covers a wider swath (562 miles or 904 km)

## Slide 11: Hurricane Odile & March Snow Storm
Hurricane Odile
Category 3, near Baja California
Sept. 15, 2014
after it made landfall
Mid-Atlantic States
Snow event,
March 17, 2014
(DC- 18 cm snow)
Transition to deep thunderstorms over the Gulf Stream
Click here for movie
Click here for movie

## Slide 12
GPM Satellites estimate precipitation but are not rain gauges
Diameter of “Best” area measurement resolution for GPM is ~3.2 miles/ 5 km
Typical Gauge diameter
4 – 12 inches/ 10 – 30.5 cm
(~2.5 billion to 270 million x smaller than a GPM pixel area!!)
Remote Sensing
Area measurement

## Slide 13
  Three Basic Approaches
  Direct Comparison (surface):
  Satellite estimates compared to rain gauge and radar products
  Physical Process: (surface and airborne)
  Improving our understanding of precipitation physical characteristics and how they relate to remote sensing
  Integrated Hydrometeorology: (surface)
  End to end evaluation of satellite and ground-based products in hydrologic/weather/climate applications
  Connecting the ground to space
  GROUND VALIDATION (GV)
Notes: An end to end tracing of GPM products, algorithm physics and product errors to water resources applications at different scales

## Slide 14
Why not just use rain gauges for GV?
“Where’s the honey?
Rain gauges are important, but only measure at a point
Gauges are weather, site, and “nature” sensitive- all affect measurement quality.
Rain is HIGHLY variable in space and time. Measuring it accurately over areas the size of satellite footprints can be challenging.
Need as few as 4 but as many as 15 gauges in a single GPM footprint to get accurate area measurement! (depends on accumulation time)
Large networks of recording gauges are required and these can be difficult/costly to maintain.
GPM Dense Raingauge Network
(25 dual-platforms in 5 x 5 km2 area)
5/30/2013: Daily rain accumulation
>250% difference!
3 miles

## Slide 15
We focus on complementary use of radars and ground networks
  Radar rain mapping over a larger area (> 10,000 km2)
  Radar Ability to “probe” clouds in 3-D at high space-time resolution
  Reference to reliable ground measurements (gauge networks)
GV Measurements required at a multitude of scales
Radars function as the “BRIDGE”
Gauge (point)
4 km - 50 km
DX
Gauge Network
(100 m – 10000 m)
Scanning radiometer/radar
100 m to 4 km
Scanning Precipitation Radar
Radar
(volume)
Satellite
(pixel, column)

## Slide 16: GPM vs. Ground Radar: Resolution matters!
GPM Overpass of NPOL Radar near NASA Wallops Flight Facility Site
Ground radars can map precipitation similar to a “dense” rain gauge network, but over a much larger area: Good for satellite comparisons
High-resolution radar data are used to study how precipitation “fills” GPM footprints and how footprints can be further “downscaled”
NPOL RADAR
150 m x 750 m
GPM Radar
5000m x 5000 m
GPM Radiometer
5000 m x 5000 m

## Slide 17
2) NOAA “Multi-Radar Multi-Sensor” http://nmq.ou.edu / 1-km2/2 min resolution
Blend of radar and rain-gauge data
We then compare highest quality data, or a ground reference, to GPM products
Direct GV: “Operational” Radar and Rainfall Measurements
1) Ground radar matching to GPM instruments (rain rates, precipitation types, sizes…..)

## Slide 18
GV vs. GPM DPR radar measurements: Rain Drops
Middleton Island, Alaska (PAIH) NEXRAD Radar August 14, 2014
Ground vs. GPM comparisons of reflectivity, rain drop sizes, and numbers- Looks good!
Radar Reflectivity
DPR
PAIH
PAIH
DPR
Rain Drop Numbers
PAIH
DPR
PAIH Precipitation Types
Melting Snow
Rain and Drizzle
Snow
Rain Drop sizes
(RAIN)
Light to moderate rain over Pacific Ocean

## Slide 19: GV vs. GPM GMI Radiometer Measurements: Rain and Snow
Post-Launch
GPM Radiometer (GMI) Precipitation Compared to GV
Generally good first results in snow and rain!!
However, also some “misses” ……(see circle)- why?
Snow
Rain
Snow
Rain

## Slide 20
Getting the Physics Right: GPM Field Campaigns
GPM Ground Validation
GPM must produce accurate precipitation estimates using remote sensing over a broad range of rain and snow conditions- difficult proposition!
Ground and airborne field measurements of precipitation physics to improve satellite-based remote sensing methods for estimating precipitation
Warm season
Rain
Cold season Snow/ice

## Slide 21
Research Aircraft
Connecting satellite, cloud and ground measurements
NASA DC-8
NASA ER-2
UND Citation
Views from ground radars, ER-2, and Citation
High Altitude “Satellite Simulators”
Cloud-Penetrating Aircraft
Cloud probes
Gust probe

## Slide 22
Radars and Radiometers on The ER-2
EXRAD Radar
Nose
HIWRAP
Pod
CoSMIR Radiometer
Pod
AMPR Radiometer
Q-Bay

## Slide 23
ER-2
Citation
Citation stays out of the strongest thunderstorm core (areas in red shown on the radar); We loop the ER-2 over the top of the severe portion of storm and then over the Citation on his return leg (sampling both heavy and lighter precipitation).
Ground-based “dual-polarimetric” radars provide us a “look” into the strongest part of the thunderstorm where the Citation cannot penetrate but the ER-2 can fly over.
Example of Working Airplanes in a Strong Thunderstorm
(IPHEx Field Experiment 2014)

## Slide 24
NASA NPOL and D3R Dual-Polarimetric Radars
Scan storms in 3-D, more accurately measure precipitation characteristics (types, numbers, sizes, rainfall rate) from the ground to tops of clouds. This provides a science reference for measurements the satellites make as they look down from space
NASA’s Research GV Radars
NPOL- S-band (10 cm wavelength)
D3R – Ka/Ku Band (0.86 and 2 cm wavelength; matches GPM DPR)

## Slide 25
Conventional
Radar (NEXRAD)
Polarimetric
Radar (ARMOR)
Ground-Based Polarimetric radars?
Better detect sizes, type, numbers of precipitation
Courtesy T. Schuur, NOAA CIMMS

## Slide 26
How do we scan with radars? (I)
Horizontal Plan Position (PPI) scanning
Send out 1100 pulses/second over a sector or full 360o scan at 1 - 20 elevation angles
Used for mapping precipitation and its variability

## Slide 27
Radar Range-Height Scanning (RHI’s) modes
Vertical cross sections or “Slices” of the atmosphere
Studying the precipitation physics a satellite “sees”
NASA NPOL and D3R Radars
How do we scan with radars? (II)

## Slide 28
Rainfall: Dual-Rain Gauge Networks
Ground State: Soil Moisture and Temperature
Dual-gauges ensure measurement consistency
Networks provide a reference for radars
Soil probes connect precipitation to ground hydrology and energy balance

## Slide 29
2D Video Disdrometer
Drop sizes, numbers ,shapes, type fallspeed
Micro Rain Radar
Vertical profile of precipitation properties
Parsivel Laser Disdrometer
Drop sizes, number, type fallspeed
Precipitation Particle Measurements
Reference for polarimetric radar estimates

## Slide 30
Operation:
Laser signal blocked when particle passes through beam
Measurement:
Particle diameters and size distribution fall speeds, types (rain, snow), precipitation rate
Parsivel Laser Disdrometer
2D Video Disdrometer
Operation:
Two perpendicular light sheets project onto line-scan cameras. Falling hydrometeors cast a shadow recorded by cameras
Measurement:
Particle diameters (2-D) and shapes, numbers, fall speeds, type (rain, snow, hail), precipitation rate

## Slide 31
Snow: Precipitation Imaging Package
Size, shape, and fall speeds of snow
Image, track, size, count, each snow crystal/flake
Systems in Virginia, Michigan, Washington, Canada, Finland

## Slide 32
Putting it all together: Radar Map of Rain
Combine ground and radar measurements for “reference” rainfall maps
Use reference maps for satellite comparisons and flood modeling studies.
Use what we learn about rainfall process to improve satellite estimations methods
“Standard” PPI of Radar Reflectivity
Radar-Derived Map of 24-Hour Rainfall

## Slide 33
“Spherical” Small Hail
Disdrometers: What did the precipitation “look” like?
Characterize rain size, shape and numbers as it falls.
~ 1/3 inch
Reference for radar identification of precipitation type and size
“Oblate” large rain drops

## Slide 34
Define the Physical Process: What satellites are “seeing”
NPOL Radar also “slices” the storm with RHI scans
Snow rimes
Graupel is formed
Graupel becomes hail and/or rain freezes and rimes to become hail
Rain drops
(melting snow, hail, graupel)
The “process” : Ice to Rain

## Slide 35
Advanced Microwave Passive Radiometer “sees” ice
50,000 foot echo top, hail core 39,000 feet, golf ball to tennis ball-sized Hail
Sampling a Deep Storm Top to Bottom
5/23/2014 Northern S. Carolina
Picture: D.S. Broce, AFRC
walt.petersen@nasa.gov
View from ER-2 at 65,000 feet
NPOL Radar: slices the storm from bottom to top
Notes: ER-2 sampling from IPHEX showing the data collection vantage point from the ER-2, with AMPR brightness temperatures and then the coinciding view from the ground via NPOL (theme here again is the “complete” picture of the physics from top to bottom). Airborne and ground-based instruments provide a complementary view.

## Slide 36
Snow from Top to Bottom 1/30-31, 2012
Left: Snow event as viewed from the air by DC-8 above, Citation Aircraft in cloud;
Right: Ground observations via radar, particle sizing instruments, and imaging
DC-8 Airborne (satellite)
Stacked Legs (DC-8/Citation)
DC-8 CoSMIR Radiometer
DC-8 APR-2 Radar
Ku
Ka
Ku
Ka
Citation Airborne (cloud)
Snow microphysics profiles
Grnd. Instruments (surface)
Regional to Particle Scale
King City
C-band Radar
D3R Radar Ku-Band
PIP Size Distributions
And images
U. Manitoba Imaging Camera

## Slide 37
Walt.petersen@nasa.gov

## Slide 38
GPM GV: Map- we are everywhere….and when we are not there we are here
Field campaigns since 2007
GV is a Global Effort!
International cooperation to connect what is observed at the ground and in the clouds (e.g., rain, snow, ice), to what is observed from space
Instruments deployed (current)
OLYMPEX Field Campaign (2015/16)
National Network
collaboration