## Slide 1: Protocol Training Slides for: Barometric Pressure

## Slide 2: The Atmosphere
Extremely thin blanket of air extending about 300 miles from Earth’s surface to edge of space
Composition of molecules of nitrogen, oxygen, argon, water vapor, carbon dioxide, and other gases
Protection from the blasts of radiation emanating from the Sun
Image: NASA

## Slide 3: This Module
Overview
This module
Describes how to take barometric pressure observations
Provides instructions on how to enter your data on the GLOBE website
Learning Objectives
After completing this module, you will be able to
Describe what barometric pressure is
List reasons why it is important to collect barometric pressure data
Determine the correct locations to take barometric pressure readings
Upload data to GLOBE website
Visualize data using GLOBE Visualization Site and formulate your own questions about weather
Estimated time to complete module: 1 hour

## Slide 4: Barometric Pressure
Measures the weight of the atmosphere per unit area
Is the weight (force) of the air pushing on each unit of surface area on the ground
Increase or decrease indicates upcoming weather change
High pressure generally brings fair weather, and low pressure is associated with “bad weather”
Link to Barometric Pressure Protocol here

## Slide 5: Recording barometric pressure is important for many reasons:
Used to predict the weather
Used to interpret measurements of aerosols, ozone, and water vapor

## Slide 6: YOUR measurements can help NASA scientists to
Understand and predict the weather (air temperature, rain, relative humidity, cloud conditions, atmospheric pressure)
Understand Atmospheric Composition (trace gases and particles in the air)
Interpret aerosols, ozone, and water vapor measurements

## Slide 7: Example: NASA’s Aquarius Mission
Studying the relationship of ocean salinity and atmospheric pressures which vary on Earth.
Image illustrates the pattern of atmospheric pressures on Earth. Atmospheric pressure highs are at the poles, 30°N and 30°S. Atmospheric lows are along the equator, 60°N and 60°S.
Cloudiness and precipitation (P) dominate bands of low pressure. At these latitudes, world's rainforests are located. Dryness and evaporation (E) dominate bands of high pressure. At these latitudes, deserts are located.
Read more here
E – Evaporation; P – Precipitation’
Image: University of Maine, Aquarius

## Slide 8: Protocol at a Glance
Instruments | Aneroid Barometer or Altimeter
Data Sheet | Integrated 1-day Data Sheet
When | Preferably, within one hour of local solar noon
Where | Classroom Wall at eye level
Other | Log book for data collection; Computer with internet connection to enter data

## Slide 9: Calibrating your Instrument: Aneroid Barometer
Calibration of Aneroid Barometer
Inspect your barometer; it will most likely have two different scales, one in millibars (or hectopascals) and one in millimeters (or centimeters) of mercury. All of your measurements for GLOBE should be taken in millibars or hectopascals (remember, these are equivalent).
Find a local reliable weather information source, which provides measurements of pressure. Compare to see if the readings are the same. Once you have obtained an accurate sea level pressure reading in millibars or hectopascals, reset your barometer to this pressure reading using a small set screw on the back of the barometer (this should only be done by the teacher!).
There is a needle that can be set to the current reading each day – you should do this each day after you take your pressure reading.
When you take tomorrow’s reading, your barometer’s set needle will read yesterday’s value, and you can instantly compare to see whether pressure is higher or lower now than the day before!
Calibrate every 6 months.

## Slide 10: Calibrating your Instrument: Altimeter
Calibrating the Altimeter
Most likely already calibrated by the factory.
Pick a location where you know the altitude from a reliable source and check the setting. If different, set the altitude.

## Slide 11: Collecting Data-1
Read the barometer to the 0.1 millibar using the black arm. This barometer reads 1006.2 mb.
For this location, the pressure has dropped over the last 24 hours.

## Slide 12: Collecting Data-2
Collect data daily, preferably within one hour of local solar noon. Record the time (local or UTC) and date on the Integrated 1-day Data Sheet.
Tap gently on the glass cover of the aneroid barometer to stabilize the needle.
Read the barometer to the nearest 0.1 millibar (or hectopascal).
Record this reading as the current pressure.
Set the “set needle” to the current pressure.

## Slide 13: Data Sheet
Enter the data on the Integrated 1-Day Data Sheet
Be sure to fill out the top: School Name, Study Site, Observer Names, Date and Time (local or UTC)
Atmosphere Data Sheet

## Slide 14: Entering Barometric Pressure Data-1
You have 3 options:
Download the Data Entry app from the App Store.
Live Entry: These pages are for entering environmental data – collected at defined sites, according to protocol, and using approved instrumentation – for entry into the official GLOBE science database.
Email Data Entry: If connectivity is an issue, data can also be entered via email.

## Slide 15: Entering Barometric Pressure Data-2
1) Go to GLOBE.gov and press enter data.

## Slide 16: Entering Barometric Pressure Data-3

## Slide 17: Entering Barometric Pressure Data- 4 and 5

## Slide 18: Entering Barometric Pressure Data- 6 and 7

## Slide 19: Entering Barometric Pressure Data- 8 and 9

## Slide 20: Retrieving Data from the GLOBE Visualization System
Click on Visualize Data
E-training is available to explore the full power of the visualization system.

## Slide 21: Viewing data on the map on the GLOBE Visualization System
Close the Welcome box and click on Add + to add a layer.

## Slide 22: Questions for YOU to Investigate
After recording your pressure readings for a month, make a graph of your pressure observations and also plot the daily precipitation. Do you see a relationship between these observations?
Is there any relationship between your data from the Cloud Protocols and barometric pressure?
Use pressure data from several GLOBE schools adjusted to sea level pressure to see if you can locate where high and low pressure areas are for a given day. How well do your findings compare with weather maps from your local newspaper or any other source?

## Slide 23: What have YOU learned?
What is barometric pressure?
Why is it important to collect barometric pressure data?
What instrument(s) is/are needed to collect barometric pressure data?
Where can I purchase the instrument(s)?
Where should I take my barometric pressure measurements?
What data do I need to collect?
How do I submit my data to GLOBE?
What can I do with the data submitted to GLOBE?

## Slide 24: FAQs 1
If we missed reading the barometric pressure for a day or more (over the weekend, holiday, vacation, etc.), can we still report the pressure today? Yes, you are only reporting today’s pressure, so please report it as often as possible.
2. I really don’t understand the difference between barometric station pressure and sea level pressure. Since weather stations are spread all over the world at many elevations, and since pressure decreases rapidly with elevation, meteorologists need a way to map horizontal pressure patterns using a constant reference altitude. The easiest way to do this is to convert all observed pressure values to sea level pressure. In GLOBE, barometric pressures are reported as sea level pressures but can be accessed and visualized as either sea level or station pressures, as the database is capable of making corrections to compensate for elevation changes.
3. Why do we have to reset the “set needle” each day? The set needle is used to identify the previous pressure reading. Using it, you can instantly compare the current pressure reading to the previous one. For example, if the pressure is lower today than yesterday, you might ask yourself if the weather is stormier?

## Slide 25: FAQs 2
  6. How accurate are these pressure readings, compared to those that might be taken with mercury barometers? Today’s aneroid barometers are not as accurate, in general, as well-made mercury barometers. There are some electronic barometers that have very accurate measurements, but the relatively inexpensive instruments that meet GLOBE specifications have all the necessary accuracy for our pressure measurements (about 3 to 4 mbar).
  7. Why does pressure always decrease with height in the atmosphere? Because pressure is a measure of the mass of the atmosphere above you (air does have mass!), as your elevation increases, there is less air above you, so pressure is less.
  8. Why do high altitude GLOBE schools have to use an altimeter? Most aneroid barometers are designed to be used near sea level. Altimeters are special aneroid barometers designed to be used at higher altitudes (including aircraft). At an altitude of 500 m above sea level, we would expect atmospheric pressure to be no greater than 1000 mbar and down to as low as 900 mbar for intense storms. Most aneroid barometers, however, have 950 mbar as the lowest possible measurement.

## Slide 26: Further Resources
  GLOBE Learning Activities
  My NASA Data
  Information on purchasing GLOBE supplies

## Slide 27: We want your feedback!
Please provide us with feedback about this module. This is a community project and we welcome your comments, suggestions and edits!
Comment here: eTraining Feedback
Do you have questions? help@globe.gov
Credits:
Power point Developers:
Kevin Czajkowski
Janet Struble
Mikell Lynne Hedley
Sara Mierzwiak
Photos unless otherwise identified:
Kevin Czajkowski
Funding Provided by NASA
Version 5/13/20. If you edit and modify this slide set for use for educational purposes, please note “modified by (and your name and date)“ on this page. Thank you